WOODPECKER CNC

Instructions

Machine size

http://www.aliexpress.com/store/1941516

Installation Instructions

1,the base installation

a) material：

| material | specification | Quantity | Number | Remark |
| --- | --- | --- | --- | --- |
| aluminum | 240mm | 2 |  |  |
| aluminum | 220mm | 2 |  |  |
| Screws | M5x10 | 8 |  |  |
| Gasket | M5 | 8 |  |  |
| Slide nut | M5 | 18 |  |  |
| Corner pieces | 2020 | 4 |  |  |

b) installation：

c) Aluminum connection

d) The final results:

Feeling installation was relatively flat, then you can put the screws a little tight, so relatively secure.

e) Precautions:

Try to find a relatively flat place during installation. Preferably in the tooling stage

Y axis Assembly：

a) material：

| material | specification | Quantity | Number | Remark |
| --- | --- | --- | --- | --- |
| Optical axis Support base | SK8 | 4 |  |  |
| straight line Optical axis | 240mm | 2 |  |  |
| Slider |  | 4 |  |  |
| Nut seat |  | 1 |  |  |
| mesa | 20100 | 1 |  |  |
| Screws | M5x10 | 18 |  |  |
| Slide nut | M5 | 10 |  |  |

b)

Optical axis seat installation results as shown: Axis spacing 120mm,It can also be adjusted according to your own ideas. Do not tighten the screws, Because you may have to fine-tune.

e) Table mounted as shown in figure:

Screw is also not too tight. The direction of the nut seat can be free, and the direction of the slider is as shown in fig..

f) The final result: in the installation, the shaft spacing can be adjusted according to the actual situation.

3，Y axis motor and lead screw assembly

- material

| material | Specifications | Number | umber | Remarks |
| --- | --- | --- | --- | --- |
| Motor mounting plate |  | 1 |  |  |
| Stepper motor | 42 | 1 |  |  |
| Coupling |  | 1 |  |  |
| Top Wire rod | M4 | 4 |  |  |
| Wire rod | 218mm | 1 |  |  |
| Copper nut |  | 1 |  |  |
| Spring |  | 1 |  |  |
| Screw | M5x10 | 2 |  |  |
| Screw | M3x6 | 4 |  |  |

b)

motor installation instructions: the coupling assembly to the motor, the motor shaft into the coupling 12.5mm, and then the top wire fixation. Install motor on the motor mounting plate, and then install the motor mounting plate on the machine,

Note that the screws on the machine do not tighten,

- Screw lever Installation instructions：

- Screw lever and Coupling installation

The final effect：

Long men frame installation

| material | Specifications | Number |  | Remarks |
| --- | --- | --- | --- | --- |
| aluminum | 220mm | 2 |  |  |
| aluminum | 200mm | 2 |  |  |
| Screw | M5x10 | 8 |  |  |
| Shim | M 5 | 8 |  |  |
| Slider nut | M5 | 9 |  |  |
| Corner pieces |  | 4 |  |  |

- The final effect：

On the back ,Set aside a nut, as shown in figure. Used to install the control board.

  - X axis installation

- materials

| materials | Specifications | Number |  | Remarks |
| --- | --- | --- | --- | --- |
| XZ Component |  | 1 |  |  |
| Motor mounting plate |  | 1 |  |  |
| Stepper motor | 42 | 1 |  |  |
| Coupling |  | 1 |  |  |
| The top Lever | M4 | 4 |  |  |
| Screw lever | 238mm | 1 |  |  |
| Copper nut | M6 | 1 |  |  |
| Spring |  | 1 |  |  |
| Screw | M5x10 | 10 |  |  |
| Screw | M3x6 | 4 |  |  |

- install XZ components. As shown in the figure, the optical axis of the top support seat edge and aluminum top align, distance between two axes 68mm, installed after asks the X axis around mobile uniform intensity.

- The final effect：

  - machine assembly

- materials

| materials | Specifications | Number |  | Remarks |
| --- | --- | --- | --- | --- |
| Screw | M5x10 | 8 |  |  |
| Shim | M5 | 4 |  |  |
| Slider nut | M5 | 8 |  |  |
| Corner pieces |  | 2 |  |  |
| Diagonal brace |  | 2 |  |  |

as shown in figure, the Longmen stand off the base of the 6mm, the reason is that such installation can make the center of the main axis of the spindle and Y axis.

- installation support

- Install control board